## Slide 1: Mosquitoes' wingbeat analysis

## Slide 2: Use case of the product
Study mosquitoes' populations
Understand the behavior of different species
Help researchers
Multiple benefits for global health

## Slide 3: System requirements
A low consumption autonomous trap
Attracts mosquitoes
Detects the presence of a mosquito
Reads and save each wingbeat
Results can be retrieved by a scientist

## Slide 4: System global view

## Slide 5: First proof of concept
DC motor to simulate the mosquitoes’ wings
Little to none modification of the pulses received as the UV beam is very narrow

## Slide 6: Second PoC
Better results as the reflective part really cuts the light beam
Realistic concept for the real system

## Slide 7: PoC results
The spikes are clearly separated from the noise
The amplitude is too low
More amplification is needed

## Slide 8: Simulation – UV LED circuit
High energy pulses
To increase the effective distance and the signal quality for the receiver
Without blowing out the LED

## Slide 9: The 555 precision timer IC
A precision timer IC
Can be used as a pulse generator
Monostable, or bistable to produce flip-flop switching action
5-15V, 200mA  suitable to drive the MOSFET

## Slide 10: Capacitor charge and discharge
Diode to bypass the resistor when charging the capacitor to get a 20% duty cycle
Two internal voltage dividers for the threshold : Vcc/3 and 2Vcc/3
That is why the capacitor charge and discharge between 1,6v and 3,3V

## Slide 11: LED current
40mA RMS  reliable limit

## Slide 12: Signal processing simulation

## Slide 13: Simulation – parameters and assumptions
Parameters used to simulate the phototransistor’s output
Period for a wingbeat frequency of 800Hz

## Slide 14: Simulation – low pass filter
Mosquitoes’ wingbeat vary between 600 and 1000Hz
We use a low pass filter to cut off the 20kHz signal from the LED (and some noise)
Cut off frequency (-3dB) of 1kHz

## Slide 15: Simulation – inverting amplifier
Voltage inverting is done to get positive voltage spikes for easier microcontroller reading
For stability with a high gain (1000), the amplification should be done with 2 or 3 stages

## Slide 16: Simulation – high pass filter
Used to delete the DC offset
Fc=160Hz at -3dB
Pulses are very short (0,2ms) so another step is needed before the IC input

## Slide 17: Peak hold circuit
To make the pulses last longer
With a Schottky diode (low voltage)
The voltage slowly decrease with R4
No more negative voltage thanks to the diode

## Slide 18: Comparator with hysteresis (Schmitt trigger)
To get binaries output for the IC with full amplitude (here +5V)
Vref=200mV if Vout=0V
Vref = 220mV if Vout=5V
Hysteresis of 20mV to prevents ripple
Resistor bridge on LTSpice but in “real life” we would use a true voltage reference (Zener)